## Slide 1
IIT Bombay
Course Code : EE 611
Department: Electrical Engineering
Instructor Name: Jayanta Mukherjee
Email: jayanta@ee.iitb.ac.in
EE 611 Lecture 10 Jayanta Mukherjee
Page 1
Lecture 10

## Slide 2
IIT Bombay
Topics Covered
Passive devices
One port devices
Two port devices
Example 2 port devices
3 Port Devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 2

## Slide 3
Passive Devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 3
IIT Bombay
We will now study various N port devices
As we consider several device types, they are classified
on the basis of the number of ports
The devices to be studied will have number of ports ranging
from 2 to 4

## Slide 4
One Port Device
EE 611 Lecture 10 Jayanta Mukherjee
Page 4
IIT Bombay
A one port device is simply a termination, with an S matrix
consisting of a single number S11
All one port devices are therefore reciprocal
If a one port device is lossless then |S11|=1
Examples are “matched”, “open” and “short” loads
Other terminations may be useful depending on need e.g
matching stubs. We saw in Chapter 3 how to build arbitrary
loads

## Slide 5
Short Termination
EE 611 Lecture 10 Jayanta Mukherjee
Page 5
IIT Bombay
A short termination is created by completely covering the
cross section of the line by a metal plane.
Otherwise some fringing fields and radiation loss will exist
and the quality of the short degrades as the frequency
increases

## Slide 6
Open Termination
EE 611 Lecture 10 Jayanta Mukherjee
Page 6
IIT Bombay
An open termination is more difficult; if a line is simply left
open to air, radiation will occur from the open line as well
as fringing capacitance and the termination quality will be
degraded.
Radiation loss can be reduced in coaxial lines by extending
the outer conductor beyond the ending point of the inner conductor
Fringing capacitance will still be a problem though

## Slide 7
Matched Load Termination
EE 611 Lecture 10 Jayanta Mukherjee
Page 7
IIT Bombay
A matched load can be created by introducing a conducting material into the line cross section
Because reflections will occur at the boundary between media, the conducting medium is introduced gradually so that the fraction of the line cross section it occupies gradually increases
In coaxial lines a cone shaped piece of conducting material can be useful

## Slide 8
Waveguide realization
EE 611 Lecture 10 Jayanta Mukherjee
Page 8
IIT Bombay

## Slide 9
Two Port devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 9
IIT Bombay
A two port device can perform numerous functions and is
the most common device type. The two by two matrix contains
4 complex parameters (8 numbers)
A reciprocal two port will be characterized by S11, S21 and
S22 (6 numbers)
A lossless two port will have
|S11|2 + |S21|2 = 1
|S12|2 + |S22|2 = 1
S11S12* + S21 S22* = 0
which requires only 5 numbers
A lossless reciprocal network is described by only 3 numbers
|S11| and the phase angles θ1, θ2 of S11 and S22

## Slide 10
Example two ports
EE 611 Lecture 10 Jayanta Mukherjee
Page 10
IIT Bombay
The simplest two-port circuit is a transmission line
Other two port-circuits include
- bends
- discontinuities
- transitions in lines: coaxial-microstrip, coaxial waveguide
- attenuator
- mode suppressor

## Slide 11
Bends
EE 611 Lecture 10 Jayanta Mukherjee
Page 11
IIT Bombay
Guidelines for realizing bends

## Slide 12
Coaxial and Co-planar Waveguide
Discontinuities
EE 611 Lecture 10 Jayanta Mukherjee
Page 12
IIT Bombay

## Slide 13
Discontinuities in Waveguides
EE 611 Lecture 10 Jayanta Mukherjee
Page 13
IIT Bombay

## Slide 14
Discontinuities in Waveguides
EE 611 Lecture 10 Jayanta Mukherjee
Page 14
IIT Bombay

## Slide 15
Transitions: SMA Launcher
EE 611 Lecture 10 Jayanta Mukherjee
Page 15
IIT Bombay
Transitions from coaxial to microstrip are called “launchers”
The narrow microstrip acts like inductance
There is also fringing capacitance on either side of the transition
Minimum VSWR is obtained for L=Z02(C1 + C2) (Butterworth Filter)

## Slide 16
Transitions: Coaxial to Waveguide
EE 611 Lecture 10 Jayanta Mukherjee
Page 16
IIT Bombay
The Coaxial cable contains TEM mode, however the rectangular
mode transmits TE10 (dominant mode)
Waveguide needs to be designed to facilitate this transition
The design shown above allows E fields to undergo this transition

## Slide 17
Transitions: Coaxial to Waveguide
EE 611 Lecture 10 Jayanta Mukherjee
Page 17
IIT Bombay
The TE10 H field is also allowed to exist in the horizontal plane
The short and λ/4 segments allow the right and left waves to
have same phase

## Slide 18
Attenuator
EE 611 Lecture 10 Jayanta Mukherjee
Page 18
IIT Bombay
An ideal attenuator is characterized by the following property:
- S11=0 and S22=0 (port 1 and 2 are matched)
- Provides a desired insertion loss L = -10 log10(P2,out/Pi,in)
=-10 log10 |S21|2
Lossy card attenuator in waveguides

## Slide 19
Attenuator
EE 611 Lecture 10 Jayanta Mukherjee
Page 19
IIT Bombay
An attenuator using transmission lines can be constructed similar
to a matched termination except that the transmission lines have
to be lossy now.
A lumped element attenuator is a simple resistive network:
Pozar provides a 3 dB example in pg 198. To obtain an arbitrary
attenuation

## Slide 20
Other devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 20
IIT Bombay
Another two-port device is a “mode suppressor” which acts to
suppress higher order modes in a given device as power
propagates from port 1 to port 2
One way of doing this is to add metal structures which are
aligned with the electric fields of a particular mode but not the
desired mode.

## Slide 21
Other devices (2)
EE 611 Lecture 10 Jayanta Mukherjee
Page 21
IIT Bombay
The undesired mode will then be reflected to port 1 while the
desired mode can propagate to mode 2
Other 2 port networks include impedance matching networks
(Ch 3), resonators (Ch 6) and filters (Ch 7)

## Slide 22
3 Port Devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 22
IIT Bombay
In a 3 port device there are 9 complex S parameters
If we would like to match all the ports i.e Sii=0 when all other
ports are terminated in matched loads. In this case the S matrix
becomes
If in addition this is a reciprocal network, S12=S21, S13=S31
and S23=S32
If this is also a lossless network, then
|S12|2+|S13|2=1 |S12|2+|S23|2=1 |S13|2+|S23|2=1
S13*S23 = S23*S12 = S12*S13 = 0

## Slide 23
Properties of 3 Port Devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 23
IIT Bombay
The previous set of equations have no solution
We need to relax at least one of these requirements to make a
realizable device
If we want a reciprocal and lossless but un-matched network
we have a “tee” junction
I we want a lossless and matched but non-reciprocal we have
a “circulator”
I we want a reciprocal and matched but lossy network, we
have a “power divider”

## Slide 24
Summary of 3 port devices
EE 611 Lecture 10 Jayanta Mukherjee
Page 24
IIT Bombay
 | Tee | Circulator | Power Divider
Lossless | X | X | 
Reciprocal | X |  | X
Matched |  | X | X