## Slide 1
IIT Bombay
Course Code : EE 611
Department: Electrical Engineering
Instructor Name: Jayanta Mukherjee
Email: jayanta@ee.iitb.ac.in
EE 611 Lecture 8 Jayanta Mukherjee
Page 1
Lecture 8

## Slide 2
IIT Bombay
Topics Covered
Impedance Matrix
Properties of Loss Less and Reciprocal Devices
Scattering Parameters
EE 611 Lecture 8 Jayanta Mukherjee
Page 2

## Slide 3
Impedance Matrix
EE 611 Lecture 8 Jayanta Mukherjee
Page 3
IIT Bombay

## Slide 4
Admittance Matrix
EE 611 Lecture 8 Jayanta Mukherjee
Page 4
IIT Bombay

## Slide 5
Reciprocal and Non Reciprocal
Materials
EE 611 Lecture 8 Jayanta Mukherjee
Page 5
IIT Bombay
For non-reciprocal medium
- semiconductor + power supply
- plasma
- Ferrite + magnetic field
The dielectric constant ε and permeability μ are non-reciprocal matrix and we have Zij ≠ Zji
For reciprocal medium we have Zij = Zji and [Z] t = [Z]

## Slide 6
Reciprocal 2 Port network
EE 611 Lecture 8 Jayanta Mukherjee
Page 6
IIT Bombay
Circuit representation of a 2 port reciprocal network

## Slide 7
Lossless Networks
EE 611 Lecture 8 Jayanta Mukherjee
Page 7
IIT Bombay
If a network is lossless (i.e. no lossy lines, no lumped
resistors, no radiation loss etc.) then
The total complex power Ptot dissipated by the N-port device
is given by
For lossless devices Re {Ptot}=0
Plugging in Ptot in the impedance matrix for Vn gives
The real part of the above has to be zero regardless of the
values of In which excite the network

## Slide 8
Consider that only one of the port currents is not zero. Say that
port is called n’ ; our previous equation is then
so the diagonal entries of the matrix must be purely imaginary
Now consider that only two currents are non zero. Call these
In’ and In”. We then get
Properties of a Lossless reciprocal
impedance matrix
EE 611 Lecture 8 Jayanta Mukherjee
Page 8
IIT Bombay

## Slide 9
Properties of a Lossless reciprocal
impedance matrix
EE 611 Lecture 8 Jayanta Mukherjee
Page 9
IIT Bombay

## Slide 10
Summary of Impedance matrix
properties
EE 611 Lecture 8 Jayanta Mukherjee
Page 10
IIT Bombay
If a network is reciprocal, the Z and Y matrices are symmetric
If a network is lossless, the diagonal impedance or admittance
matrix elements are purely imaginary
If a network is lossless and reciprocal, all impedance or
admittance matrix elements are purely imaginary

## Slide 11
Scattering Parameters
EE 611 Lecture 8 Jayanta Mukherjee
Page 11
IIT Bombay
S-parameters can be measured with a network analyzer
They have a natural relation with the flow of power
S-parameters are readily represented by flow-graph
The measurement of S-parameters relies on 50 ohm resistive
terminations: usually active devices do not oscillate for such
terminations
Devices are measured in the medium in which they are used

## Slide 12
Normalized waves, voltages and
currents
EE 611 Lecture 8 Jayanta Mukherjee
Page 12
IIT Bombay

## Slide 13
Normalized waves, voltages and
currents
EE 611 Lecture 8 Jayanta Mukherjee
Page 13
IIT Bombay

## Slide 14
Normalized Z matrix
EE 611 Lecture 8 Jayanta Mukherjee
Page 14
IIT Bombay

## Slide 15
Definition of Scattering Parameters
EE 611 Lecture 8 Jayanta Mukherjee
Page 15
IIT Bombay

## Slide 16
2 port scattering parameters
EE 611 Lecture 8 Jayanta Mukherjee
Page 16
IIT Bombay

## Slide 17
S Matrix properties
EE 611 Lecture 8 Jayanta Mukherjee
Page 17
IIT Bombay
Reciprocal devices have symmetric impedance matrices, and
that lossless reciprocal devices have purely imaginary
impedance matrices
Let’s find similar identities for S matrix
Our normalized impedance matrix equation is
[V] = [Z] [I]
Now since [V] = [a] + [b] and since [I] = [a] - [b] we get
[U] ([a] + [b]) = [Z] ([a] - [b])
Where [U] is the identity matrix

## Slide 18
S Matrix properties (2)
EE 611 Lecture 8 Jayanta Mukherjee
Page 18
IIT Bombay
We can also get another similar relationship using
[a] = (1/2) { [V] + [I] } = (1/2) { [Z] + [U] } [I]
[b] = (1/2) { [V] – [I] } = (1/2) { [Z] – [U] } [I]
Re-write as
{ [Z] + [U] } [b] = { [Z] – [U] } [a]
Now since we define our S-matrix through [b] = [S] [a], we
find
[S] = { [Z] + [U] }-1 { [Z] - [U] } (1)
which is the relation between the normalized Z and S matrices

## Slide 19
S Matrix properties (3)
EE 611 Lecture 8 Jayanta Mukherjee
Page 19
IIT Bombay
Solving the above equations for [b] in terms of [a], we find
[b] = { [Z] - [U] } { [Z] + [U] }-1 [a]
So another formula for the S matrix is
[S] = { [Z] – [U] } { [Z] + [U] }-1 (2)
Taking the transpose of (1) we get
[S] t = { [Z] + [U] }-1 t { [Z] – [U] }t
but [U] and [Z] are symmetric if the medium is reciprocal so
[S]t = { [Z] + [U] }-1{ [Z] – [U] }

## Slide 20
S Matrix properties (4)
EE 611 Lecture 8 Jayanta Mukherjee
Page 20
IIT Bombay
Since this is the same as our equation (2) this means that the S
matrix is symmetric for a reciprocal medium [S] = [S]t

## Slide 21
S Matrix for a lossless medium
EE 611 Lecture 8 Jayanta Mukherjee
Page 21
IIT Bombay
In a lossless device, the sum of all power entering and exiting
must be zero.

## Slide 22
S Matrix for a lossless medium
EE 611 Lecture 8 Jayanta Mukherjee
Page 22
IIT Bombay
On the previous slide we obtained
[a]t [U] [a]* = [a]t [S]t [S]* [a]*
Simplifying we get [a]t { [U] – [S]t [S]* } [a]* = 0
Since this is true regardless of what values the elements of [a]
take , we have [S]t [S]* = [U] which is equivalent to saying
that S is “unitary” : [S]H = [S]-1
This is most conveniently expressed in terms of elements of S
as

## Slide 23
Reverse Time Symmetry
EE 611 Lecture 8 Jayanta Mukherjee
Page 23
IIT Bombay
Refers to the concept that if time could be reversed then the
incident and reflected waves would main the exact same
relation at any two ports
Since however the direction of propagation is reversed we need
to take the conjugate and so the relation between [a] and [b]
becomes
[a]* = [S] [b]*

## Slide 24
Reciprocity of Lossless Devices
EE 611 Lecture 8 Jayanta Mukherjee
Page 24
IIT Bombay
We have demonstrated that [S] is unitary for lossless devices
Using time reversal symmetry: if [b] = [S] [a] then [a]* = [S] [b]*
It results that:
[a]* = [S] [b]* = [S] [S]* [a]* → [S]* = [S] -1
Now since the device is lossless we also have:
[S]* = [S] -1 = [S]H → [S] = [S] t
It results that a lossless device whose response is invariant
under time reversal symmetry has a reciprocal [S] matrix

## Slide 25
Shifting reference planes for lossless
lines
EE 611 Lecture 8 Jayanta Mukherjee
Page 25
IIT Bombay

## Slide 26
Shifting reference planes for lossless
lines
EE 611 Lecture 8 Jayanta Mukherjee
Page 26
IIT Bombay

## Slide 27
Shifting reference planes for lossless
lines
EE 611 Lecture 8 Jayanta Mukherjee
Page 27
IIT Bombay

## Slide 28
3 Port example
EE 611 Lecture 8 Jayanta Mukherjee
Page 28
IIT Bombay